System Identity

---
What makes one node different from an other?
What makes one node different from an other?
- Hostname
- IP Address
- Link-Level Address

---
Link-Level Address
Link-Level Address
- Hardware, Ethernet, or MAC address
- Should be globally unique
- Must be unique within a LAN segment
- Set by hardware vendor at the factory
- Set by VirutalBox software -> easy to have duplicates!!!

---
Inspect Link-Level Address
Inspect Link-Level Address
# ip link
Sample output from w01:
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN mode DEFAULT group default qlen 1000
    link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00
2: enp0s3: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP mode DEFAULT group default qlen 1000
    link/ether 08:00:27:48:be:6b brd ff:ff:ff:ff:ff:ff
3: enp0s8: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP mode DEFAULT group default qlen 1000
    link/ether 08:00:27:b4:2e:91 brd ff:ff:ff:ff:ff:ff
MAC Address
Device name

---
IP Address
IP Address
- IP-V4 or IP-V6
- Must be unique within the Internet (aka the “open internet”)
- Special addresses deemed “non-routable”
  - 10.0.0.0/8 (255.0.0.0)
  - 172.16.0.0/12 (255.240.0.0)
  - 192.168.0.0/16 (255.255.0.0)
  - These use NAT when connecting to the Internet

---
Inspect IP Address
Inspect IP Address
# ip addr
Sample output from w01:
﻿﻿﻿1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN
     link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00
     inet 127.0.0.1/8 scope host lo inet6 ::1/128 scope host
        valid_lft forever preferred_lft forever
2: enp0s3: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP qlen 1000
    link/ether 08:00:27:56:ce:36 brd ff:ff:ff:ff:ff:ff
    inet 10.0.2.15/24 brd 10.0.2.255 scope global eth0
    inet6 fe80::a00:27ff:fe56:ce36/64 scope link
        valid_lft forever preferred_lft forever
3: enp0s8: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP qlen 1000
    link/ether 08:00:27:a3:c4:37 brd ff:ff:ff:ff:ff:ff
    inet 10.1.1.10/24 brd 10.1.1.255 scope global eth1
    inet6 fe80::a00:27ff:fea3:c437/64 scope link
        valid_lft forever preferred_lft forever
How many NICs does w01 have?
Are any on the Open Internet?
What is 127.0.0.1?

---
Set Address
Managing Network Connections
Interactively with ip command
  - Will not survive a reboot
- Network Manager program
  - GUI, TUI, or CLI
  - Default for RHEL 8
- Configuration files
  - Suitable for some servers
  - Popular with ‘old admins’ and Debian

---
Network Manager
- Runs as a daemon
- We tell the daemon what to do with one of three programs
  - GUI (Graphical User Interface)
  - TUI (Text User Interface)
  - CLI (Command Line Interface)

---
Network Manager - Terms
Device – a network or WIFI card (can be a virtual device)
Connection – a set of configuration settings which can be applied to a device
Connections are applied to devices.
Most servers have a one and only one connection per device.

---
CLI - Operations
Stop all networking
nmcli networking off
Start all networking
nmcli networking on
Show all connections
nmcli connection show
Stop one connection
nmcli connection down enp0s3
Start one connection
nmcli connection up enp0s3

---
CLI – Operations (cont)
Show details for one connection
nmcli connection show enp0s3
Set a static IP address for enp0s3
nmcli connection modify enp0s3 ipv4.method manual
nmcli connection modify enp0s3 ipv4.addresses 10.1.1.20/24
Set enp0s3 to be a DHCP client
nmcli connection modify enp0s3 ipv4.method auto

---
Hostname
Hostname
- One per system
- Can be anything, usually:
w01.example.com
Or
W01
No direct link to IP address

---
Set hostname
Set hostname
Run the hostname command
  - Will not survive a reboot
- Define in the /etc/hostname file
  - Read by start up scripts
  - Requires reboot
- Use Network Manager
nmcli general hostname s01

---
Nice names with /etc/hosts
Nice names with /etc/hosts
- Simple file to map human friendly names to IP addresses and back
- Suitable for small, internal networks
- Does not scale well

---
Sample:
Sample:
# cat /etc/hosts
127.0.0.1 localhost localhost.localdomain localhost4
::1 localhost localhost.localdomain localhost6
10.1.1.20 s01
10.1.1.10 w01 wAlice
IP Address
List of names (do not need to match host names)

---
udev
udev
- Device manager for the kernel
- Tries to keep device names (enp0s3, enp0s8) constant
- Network card device names are based on hardware location

---
Reference
Man pages of interest
  man ip
  man nmcli